## Slide 1: Project Presentation Digital Image Processing – EESC6363
Parth Parikh ( 2021165845)
Department of Electrical Engineering
University of Texas at Dallas

## Slide 2: Objective
To implement pre-processing and post-processing algorithms to perform image deblurring, followed by qualitative and quantitative analysis of the results.

## Slide 3: Introduction
Image blur is persistent in most images, when the camera is hand held. The blur may vary from being an acceptable bokeh to values that can ruin the photograph.
This project simulates two image deblurring techniques that have been successfully accomplished previously; and performs a comprehensive comparison of the result. Here, both subjective and objective methods have been used to evaluate the deblurred images.

## Slide 4: Image Deblurring Techniques
Auto Tonal Correction
Blind Deconvolution
Computationally efficient.
Suitable for cell phone platform
No prior assumptions made about the motion
Mimics statistics of blurred image onto low exposure image
Estimates PSF mask based on data from inertial sensors
Assumes that there is no motion in the z-direction and the focal length of the camera is constant
Employs blind wiener deconvolution to deblur image

## Slide 5: Image Deblurring Techniques (contd..)
Auto Tonal Correction
Blind Deconvolution
Important functions
f performs correction in the mean.
g performs correction in the variance
C is the final psf mask, where and are the position vectors in x and y
U, G and H are fourier transforms of deblurred image, blurred image and PSF resp.

## Slide 6: Aparatus
In order to accomplish the task at hand the following two devices were used:
  Nikon® D3100 Apple® iPhone
    18-55 VR AF Lens To capture inertial sensor
    Most shots taken at 1/40 sec data using app: Pocket IMU

## Slide 7: Results and Analysis
After applying the algorithms on 50 images, varied results have been observed.
Average Performances of which are mentioned below:
Parameter | ATC Method | PSF Method | Proposed
Subjective Rating | 7.281 | 2.530 | 7.254
MSE | 131.171 | 86.698 | 25.955
Time taken | 2.066 minutes | 0.659 minutes | 1.776 seconds

## Slide 8: Sample Results

## Slide 9
BLURRED IMAGE

## Slide 10
LOW EXPOSURE IMAGE

## Slide 11
ATC CORRECTED IMAGE

## Slide 12
PSF DEBLURRED IMAGE

## Slide 13
DEBLURRED USING PROPOSED ALGORITHM

## Slide 14
BLURRED IMAGE

## Slide 15
LOW EXPOSURE IMAGE

## Slide 16
ATC CORRECTED IMAGE

## Slide 17
PSF DEBLURRED IMAGE

## Slide 18
DEBLURRED USING PROPOSED ALGORITHM

## Slide 19
BLURRED IMAGE

## Slide 20
LOW EXPOSURE IMAGE

## Slide 21
ATC CORRECTED IMAGE

## Slide 22
PSF DEBLURRED IMAGE

## Slide 23
DEBLURRED USING PROPOSED ALGORITHM

## Slide 24
BLURRED IMAGE

## Slide 25
LOW EXPOSURE IMAGE

## Slide 26
ATC CORRECTED IMAGE

## Slide 27
PSF DEBLURRED IMAGE

## Slide 28
DEBLURRED USING PROPOSED ALGORITHM

## Slide 29: Statistics
Following slides contain few statistics that summarize the efficacy of the methods.

## Slide 30
SUBJECTIVE EVALUATION

## Slide 31
OBJECTIVE EVALUATION: Mean Square Error

## Slide 32
OBJECTIVE EVALUATION: % Error in Variance

## Slide 33
OBJECTIVE EVALUATION: % Error in Mean

## Slide 34
OBJECTIVE EVALUATION: Time Efficiency

## Slide 35: Conclusion and Inference
Consistent performance of Adaptive Tonal Correction
However, ATC gives poor results in cases where the original image itself is dark.
ATC, performs mimicking of image statistics and hence there is minimum (if not negligible distortion).
Access to accurate and exact inertial data might yield images as expected using PSF method.
Due to inaccuracy of the data and high number of assumptions in the present scenario result in ringing in the output image.

## Slide 36: Future Work
Aim to merge presently proposed technique and ATC to yield faster results that are coherent in both mean (brightness) and variance (contrast) of the blurred image.